## Slide 1: HARDWARE COMPONENTS
Instructor: john ortiz
Lecturer III utsa
stego@satx.rr.com
CS 3843 computer organization

## Slide 2: Logical Operations Review
NOT
  Invert all the bits
  One’s complement
(N) AND
  All inputs must be 1 for result to be one
  Think multiplication: 1 * 1 * 1 * 1 * … if any one of the inputs is a zero, the result is zero
  For NAND, same thing except result is inverted
    If any one of the inputs is a zero, the result is a one

## Slide 3: Logical Operations Review
(N) OR
  If any input is a one, the result is a one
  Think addition, but the result is either zero or not zero
    In order for the final result to be zero, all inputs must be zero
  For NOR, same thing except result is inverted
    In order for the final result to be one, all inputs must be zero
(XOR / XNOR)
  If both inputs are the same, the result is zero
  Think even vs. odd – even number of ones, result is zero
  XNOR is also called “equivalence” because if the inputs are the same , the result is a one

## Slide 4: Logical Operations Review
Bitwise logical operations
  Operates on each bit as specified below
NOT
  ! 0 = 1
  ! 1 = 0
AND OR
  0 & 0 = 0 0 & 0 = 0
  0 & 1 = 0 0 & 1 = 1
  1 & 0 = 0 1 & 0 = 1
  1 & 1 = 1 1 & 1 = 1
XOR
  0 & 0 = 0
  0 & 1 = 1
  1 & 0 = 1
  1 & 1 = 0

## Slide 5: The XOR Gate
An XOR gate can be constructed from basic logical operations such as the two examples below
A | B | OUT
0 | 0 | 0
1 | 0 | 1
0 | 1 | 1
1 | 1 | 0

## Slide 6: Hardware Logic
A brief look at the hardware that makes a computer work is based on the logical functions:
  NOT
    inverter
  (N) AND
    Enable / disable - (a one on one input enables the other)
    Mask bits: AND a register with 0x0000000F and all bits except bottom 4 are zero – i.e. masked off
  (N) OR
    Enable / disable - (a zero on one input enables the other)
    Mask bits: OR a register with 0x0000000F to ensure bottom 4 bits are one
  Exclusive-OR (XOR) / Exclusive-NOR (XNOR)
    Controllable inverter – (a one on one input inverts the other, a zero on one input does not)

## Slide 7: Logical – Half Adder
For binary arithmetic, XOR is an adder
  0 + 0 = 0; 0 xor 0 = 0
  0 + 1 = 1; 0 xor 1 = 1
  1 + 0 = 1; 1 xor 0 = 1
  1 + 1 = 2; 1 xor 1 = 0
    Wait! 2 is not equal to zero!
    But there is no “2” in binary, so it is expressed as 10 <one-zero>
    Soooooo, the last digit is a ZERO as in the 1 xor 1
    The 1 in the 2’s place is the carry out of adding 1 + 1
      1 + 1 = zero, carry the one  10
      Just like in decimal arithmetic: 1 + 9 = ten == 0 carry the 1  10
    We can generate a carry in hardware by AND’ing the two inputs
    Only when they are both one is the result a 1
      1 and 1 = 1

## Slide 8: Hardware: Full Adder
The prior circuit was a one-bit half adder because it did not allow for a carry in
Adding a carry in and a little extra circuitry, we construct a one-bit full adder as shown below

## Slide 9: Hardware: 4-Bit Full Adder
For multiple bits, cascade them together in parallel
Shown is a 4-bit full adder
But what about subtraction?
Of course we can build a subtractor
But better is to invert the sign of the
B input (i.e. neg B)
Taking two’s complement requires
inverting all the bits and adding one
XOR is a controllable inverter

## Slide 10: Hardware: Addition & Subtraction
But what about subtraction?
Tie the first carry in to an
“Add/Sub” signal
If that is a ONE, all the bits
will be inverted and
we will add the negative
Initial carry in is the Add One

## Slide 11: Sign Flag in Hardware
SF – Most Significant Bit (MSB)
With a 4-bit adder, this is bit #3
  Remember the Jedi mind trick:
    Always start with ZERO
    Bit #0 is the Least Significant Bit (LSB)
How do we know this is the MSB?
Cin

## Slide 12: Carry Flag in Hardware
CF – Most significant carry out with a twist
  I only recently realized the twist
  FINALLY found validation online – most sources don’t mention it
If just an adder, then most significant carry out, BUT …
If subtractor, must flip it when subtracting!
Cin

## Slide 13: Zero Flag in Hardware
ZF – Is a one when result is zero
Must capture ALL SUM bits to know if zero
An “OR” gate will be zero if all zeros – one in any other case
We want one, oh what can we do?
Cin

## Slide 14: Zero Flag in Hardware
ZF – Is a one when result is zero
Must capture ALL SUM bits to know if zero
An “OR” gate will be zero if all zeros – one in any other case
We want one, oh what can we do?
NOT OR  NOR!
Cin

## Slide 15: Zero Flag in Hardware
ZF – Is a one when result is zero
Must capture ALL SUM bits to know if zero
An “OR” gate will be zero if all zeros – one in any other case
We want one, oh what can we do?
NOT OR  NOR!
Cin

## Slide 16: Overflow Flag in Hardware
OF – Detects carry out for a signed number
When the two most significant carry out values are different, overflow has occurred
Cin

## Slide 17: Other Hardware Components
Multiplexer
Demultiplexer
Encoder
Decoder
D Flip Flop
  Gated
  Positive edge-triggered
  Negative edge-triggered
Registers
Shift Register
Counter
Transmission Gate

## Slide 18: Multiplexer
A multiplexer selects one of many inputs to be routed to the output
  n = number of inputs
  m = number of control bits
  Log2(n) = m
  2m = n

## Slide 19: Multiplexer
How many control bits required by a 4-to-1 mux?
How many control bits required by a 8-to-1 mux?
How many control bits required by a 16-to-1 mux?

## Slide 20: Multiplexer
How many control bits required by a 4-to-1 mux?
  2
How many control bits required by a 8-to-1 mux?
How many control bits required by a 16-to-1 mux?

## Slide 21: Multiplexer
How many control bits required by a 4-to-1 mux?
  2
How many control bits required by a 8-to-1 mux?
  3
How many control bits required by a 16-to-1 mux?

## Slide 22: Multiplexer
How many control bits required by a 4-to-1 mux?
  2
How many control bits required by a 8-to-1 mux?
  3
How many control bits required by a 16-to-1 mux?
  Are you kidding? If YOU can’t figure this one out by now, drop the class!

## Slide 23: Multiplexer
A simple “mux” selects between 1 of 2 inputs
  One control bit is used, it is either 0 or 1
  Log2(#inputs) = #control bits required
A 2-to-1 mux is shown below
When the ‘X’ control bit is zero, which input is routed to output ‘Y’?

## Slide 24: Multiplexer
A simple “mux” selects between 1 of 2 inputs
  One control bit is used, it is either 0 or 1
  Log2(#inputs) = #control bits required
A 2-to-1 mux is shown below
When the ‘X’ control bit is zero, which input is routed to output ‘Y’?
  X = 0 disables B and enables A

## Slide 25: Multiplexer
The full truth table for the 3 mux inputs is shown
What would we need to change such that X=1 would select the A input?
X | A | B | Y
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 26: Multiplexer
The full truth table for the 3 mux inputs is shown
What would we need to change such that X=1 would select the A input?
  Put the X input directly to the A, AND gate
  and the inverted X to the B, AND gate
X | A | B | Y
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
swap

## Slide 27: Multiplexer
4-to-1 Mux shown below
  6 inputs, 4 data (I0 – I3), 2 control (S0, S1)
  1 output, Z
  How many entries required for a full truth table?
Let’s walk through the logic

## Slide 28: Multiplexer
You may also use a block diagram for a mux and use a truth table as shown

## Slide 29: 8-to-1 Multiplexer

## Slide 30: 8-to-1 Multiplexer

## Slide 31: Multiplexer
This slide intentionally blank …

## Slide 32: Demultiplexer
A “demux” performs the exact opposite function: routes one input to one of many outputs
A simple 1-to-2 Demux is shown
  If the select line is zero, Y0 will be enabled (Y0==D) and Y1, disabled, Y1==0
  If select is one, Y1 == D, Y0==0

## Slide 33: Demultiplexer
1-to4- Demux
In this case, ‘F’ is routed to either of A, B, C, D
  Inputs a,b select which output
How many select lines if the
demux has 8 outputs?

## Slide 34: Demultiplexer
1-to4- Demux can also be made with 3, 1-to-2 demuxes
The right most image shows a demux with enable

## Slide 35: Demultiplexer
This slide intentionally blank …

## Slide 36: Encoder
An encoder takes multiple input lines and based on the one that is asserted, converts it to a binary number
  A few implementations
  The assumption is that only one of the inputs is high and the rest are low
    The middle one is supposed to be a “priority” encoder. If A3 is high, the rest don’t matter. If A2 is high (and A3 is low) the rest should not matter, BUT A1 does – let’s fix it!

## Slide 37: 4-to-2 Encoder
High level block diagram and truth table
  I do not know why one of the inputs is labeled ‘D’

## Slide 38: 4-to-2 Priority Encoder
High level block diagram and truth table
  If I3 is a one, output will be 112.
  If I2 is a one (I3 is low of course, since it has priority), then I1 and I0 don’t matter, output is 102.
One application might be a peak level detector

## Slide 39: Encoder
This slide intentionally left blank …

## Slide 40: Decoder
A decoder takes a binary number input and sets one output high <or low> based on that number
A simple 1-to-2 decoder circuit
  If A is a zero, D0 is a one, otherwise D1 is a one
A 2-to-4 Decoder should look familiar
 What is that 

## Slide 41: Decoder
And check this out … our prior 4-to-1 mux
MUX
DEMUX
DECODER

## Slide 42: Decoder
3-to-8 Decoder

## Slide 43: Decoder
This slide intentionally left blank …

## Slide 44: Flip Flops
A flip flop is a device that can store 1 bit
  It is NOT memory – memory is a different (multiple) technologies
There are also latches, which are similar to flip flops, the difference being is that a flip flop is clocked
  Latches are asynchronous – no clock
  Flip flops are synchronous with a clock
There are several types of flip flops
  S-R flop flop (Set / Reset)
  D flip flop (Data)
  T flip flop (Toggle)
The D flip flop is the building block of registers so that is our focus

## Slide 45: Flip Flops
The circuits we have studied thus far are “combinational”
  Means that when the input changes, a short time later, the output changes
  I say “a short time” because physical circuits, fast as they are, take physical time to change states
  The time it takes for the output to change, once the input changes, is called “propagation delay”
    Today, these delays are on the order of nanoseconds

## Slide 46: Flip Flops
Latches and flip flops are not combinational
They are sequential and their inputs depend on their outputs
  This is called feedback – tying an output back to an input
What do you think would happen in the following circuit?

## Slide 47: Flip Flops
Latches and flip flops are not combinational
They are sequential and their inputs depend on their outputs
  This is called feedback – tying an output back to an input
What do you think would happen in the following circuit?
It would oscillate with a period of the propagation delay
  Frequency (Hz) = 1 / period (seconds) == cycles/second
    f = 1 / T
  A low input yields a high output which now becomes the input which leads to a low output which now …
T

## Slide 48: Flip Flops
D Latch – Let’s analyze
D Flip Flop – Let’s analyze

## Slide 49: Master-Slave D Flip Flop
Those were great but we want to be able to write at the same time we are reading
One way is to cascade two flip flops together
  This is called the master-slave configuration
  This is a 1 bit register
  It is called “edge-triggered”
    More precisely, positive edge-triggered since the output changes with the rise of the clock
Note: this is
“NOT” clk,
- the inverse
of clk

## Slide 50: Master-Slave D Flip Flop
When the clock is low, the slave is in “latch” mode and does not accept input
The master changes as the input D changes
When the clock goes high, the master is latched and the slave changes according to the master
  This is called “edge-triggered” as the slave changes when the clock rises
  How would we make it negative edge-triggered?

## Slide 51: Master-Slave D Flip Flop
The flip flop is often shown as below
  This appears to be positive edge-triggered flip flop, but you really can’t tell without seeing the internal circuitry
The truth table shows how the changes in clock affect the outputs
Clock | D | Q | Q not | Description
↓ >>0 | X | Q | Q | No Memory change
↑>>1 | 0 | 0 | 1 | Reset Q>>0
↑>>1 | 1 | 1 | 0 | Set Q>>1
1
2

## Slide 52: 4-Bit Register
By cascading edge-triggered flip flops, we create a register
  The term “latch” is used incorrectly in this diagram as there is a clock
A 4-bit register is shown
  Can anyone figure out how to make a 32-bit register?

## Slide 53: 4-Bit Shift Register
As each clock pulses, the flip flop on the right gets the data from the flop flop to its left
  For a logical shift, the data in will be zeros
  For an arithmetic shift, the data in will be … you tell me?

## Slide 54: 4-Bit Shift Register
As each clock pulses, the flip flop on the right gets the data from the flop flop to its left
  For a logical shift, the data in will be zeros
  For an arithmetic shift, the data in will be … you tell me?
    No
    No
    Yes!
      I figured there would be a few wrong answers and then a correct one

## Slide 55: Toggle Flip Flop & Counters
A couple of ways to make a toggle flip flop
  For the counter below, which flip flop is the MSB?

## Slide 56: Transmission Gate
A transmission gate is nothing more than a switch
  When the switch is closed, the T-gate allows the signal through
  When the switch is open, the signal is blocked
The difference between this and enabling a combinational circuit is that the output is “high impedance” when the switch is off
  It’s as if there is no circuit there
  You can connect multiple outputs and not interfere with each other

## Slide 57: Summary of Skills
Logical Operations & Relevant Hardware
i.e. What IS on the test!!!

## Slide 58: Questions & Comments

## Slide 59: References
My brain